## Slide 1: Ribbed, Waffle, & Hollow Blocks Slabs
Lecture (4)

## Slide 2: Ribbed Slabs
Introduction
In long span, solid reinforced concrete slabs, e.g. greater than 5 m, the self-weight
becomes excessive when compared to the applied dead and imposed loads, resulting in an
uneconomic method of construction. One method of overcoming this problem is to use
ribbed slabs which are suitable for longer spans supporting light loading, as in residential
or commercial properties. They are not suitable for heavy loading such as that found in
warehouses, etc.
Ribbed slabs are reinforced concrete slabs in which some of the volume of concrete
below the neutral axis (i.e. the area in tension) is removed and replaced with block formers
or left as voids, as shown in Figures 5.90 to 5.92. The resulting construction is
considerably lighter than a solid cross-section.

## Slide 3: Continued

## Slide 4: Continued
The term ribbed slabs is defined in Clause 3.6.1.1 in BS 8110:Part 1 as slabs cast in-situ
in one of the following ways:

## Slide 5: Continued

## Slide 6: Continued
1) as a series of concrete ribs cast in-situ between blocks which remain part of the completed structure; the tops of the ribs are connected by a topping of concrete of the same strength as that used in the ribs; 2) as a series of concrete ribs with topping cast on forms which may be removed after the concrete has set; 3) with a continuous top and bottom face but containing voids of rectangular, oval or other shape.
b) Where topping is not considered to contribute to structural strength: as a series of concrete ribs cast in-situ between blocks which remain part of the completed structure; the tops of the ribs may be connected by a topping of concrete (not necessarily of the same strength as that used in the ribs). The requirements for the hollow or solid blocks and formers when required to contribute to the structural strength of a slab are given in Clause 3.6.1.2 : a) they must be made of concrete or burnt clay; b) they must have a characteristic strength of at least 14 N/mm2, measured on the net section, when axially loaded in the direction of compressive stress in the slab; c) when made of fired brick, earth, clay or shale, they must conform to BS 3921. ribs).
5.12.2 Spacing and Size of Ribs (Clause 3.6.1.3) In-situ ribs should be spaced at centres not exceeding 1.5 m and their depth, excluding any topping, should not exceed four times their width. The minimum width of rib will be determined by considerations of cover, bar spacing and fire. The minimum dimensions for fire resistance for various reinforced concrete members is given in Figure 3.2 of BS 8110:Part 1:1997.

## Slide 7: Continued
5.12.3 Thickness of Structural Topping (Clause 3.6.1.5)
The thickness of topping used to contribute to structural strength should not be less than
the value given in Table 3.17 of the code.
In hollow block slabs where the topping is not used to contribute to structural strength
the requirements of Clause 3.6.1.6 should be satisfied. They are:

## Slide 8: Continued
‘When a slab is constructed to b) of Table 3.17 the blocks should conform to 3.6.1.2. In addition the thickness of the block material above its void should be not less than 20 mm nor less than one-tenth of the dimension of the void measured transversely to the ribs. The overall thickness of the block and topping (if any) should be not less than one-fifth of the distance between ribs.’ 5.12.4 Deflection (Clause 3.6.5) The deflection of one-way spanning ribbed slabs is checked using the same method as for T-beams, i.e. span/effective depth ratios, except that the rib width may include the walls of the blocks on both sides of the rib. 5.12.7 Design Resistance Moments (Clause 3.6.3) The same procedure as used for designing beams, i.e. Clause 3.4.4, is used to determine the ultimate moment of resistance. Allowance can be included for the contribution made by the burnt clay or solid blocks in the compression zone, as indicated in Clause 3.6.3. 5.12.8 Design Shear Stress (Clause 3.6.4.2 to Clause 3.6.4.7) The design shear stress, v, should be calculated using Equation 22, which is the same as Equation 3 given in Clause 3.4.5.2 for beams. The enhancement to the shear strength from hollow blocks, solid blocks and joints between narrow precast units can be evaluated using Clauses 3.6.4.3, 3.6.4.4 and 3.6.4.5 respectively. It is sometimes necessary to make a section of the slab solid near the end supports or at other locations where high shear forces occur.

## Slide 9: Example
5.12.9 Example 5.23: Single Span Hollow-Tile Floor
A hollow-tile floor, in which the permanent blocks are not jointed in a cement:sand
mortar, is to be designed as a series of simply supported spans as indicated in
Figures 5.95(a) and (b). Using the design data given and assuming that the blocks do not
contribute to the strength of the floor, determine:
i) the suitability of the slab thickness,
ii) the reinforcement required.
Design Data:
Characteristic dead load (including self-weight) 5.0 kN/m2
Characteristic imposed load 4.0 kN/m2
Characteristic concrete strength (fcu) 40 N/mm2
Characteristic of reinforcement (fy) 460 N/mm2
Exposure condition, mild
Fire rating Minimum, 1 hour
Span of slab 4.0 m
Nominal maximum aggregate size 14 mm

## Slide 10: Continued

## Slide 11: Continued

## Slide 12: Continued

## Slide 13: Continued

## Slide 14: Continued

## Slide 15: Continued

## Slide 16: Cotinued

## Slide 17: Continued

## Slide 18: Contiued

## Slide 19: General
With medium to long spans and light to moderate live loads from 3 to 5 kN/m2, it is more economical to provide ribbed slabs constructed using glass reinforced polyester, polypropylene or encapsulated expanded polystyrene moulds (Fig. 3.55). Such slabs have reduced self-weight compared to solid slabs since part of the concrete in the tension zone is omitted. However, ribbed slabs have higher formwork costs than the other slabs systems mentioned above and, generally, they are found to be economic in the range 8 to 12 m. With the emphasis on speed of erection and economy of construction, the use of precast concrete floor slabs is now also popular with both clients and designers. Fig. 3.56 shows two types of precast concrete units that can be used to form floors. The hollow core planks are very common as they are economic over short, medium and long spans. If desired the soffit can be left exposed whereas the top is normally finished with a levelling screed or appropriate flooring system. Cranage of large precast units, particularly in congested city centre developments, is the biggest obstacle to this type of floor construction. The span ranges quoted above generally assume the slab is supported along two opposite edges, i.e. it is one-way spanning (Fig. 3.57). Where longer in-situ concrete floor spans are required it is usually more economical to support the slab on all four sides. The cost of supporting beams or walls needs to be considered though. Such slabs are referred to as two-way spanning and are normally designed as two-dimensional plates provided the ratio of the length of the longer side to the length of the shorter side is equal to 2 or less (Fig. 3.58).

## Slide 20: Ribbed Slab