## Slide 1: Prestressed Concrete
Lecture 3

## Slide 2: Pressure Line or ‘Thrust Line’, and Internal Resisting Couple
-At any given section of a prestressed concrete beam, the combined effect of the prestressing force and the externally applied load will result in a distribution of concrete stresses that can be resolved into a single force. The locus of the points of application of this resultant force in any structure is termed as the ‘pressure or thrust line.’ - The location of the pressure line depends upon the magnitude and direction of the moments applied at the cross-section and the magnitude and distribution of stress due to the prestressing force. - The load is of such magnitude that the bottom-fiber stress at the central span section of the beam is zero.

## Slide 3: Location of The Pressure Line
Observations From Fig 4.9 lead to the following important principle: “A change in the external moments in the elastic range of a prestressed concrete beam results in a shift of the pressure line rather than in an increase in the resultant force in the beam.”

## Slide 4: Reinforced & Prestressed Beams
The load-carrying mechanism is comprised of a constant force with a changing lever arm, as in the case of prestressed concrete sections, and a changing force with a constant lever arm prevailing in reinforced concrete sections as shown in Fig. 4.10. However, if a prestressed concrete member is cracked; it behaves in a manner similar to that of a reinforced concrete section.

## Slide 5: Shift of The Pressure Line
If M = Bending moment at the section due to dead and live loads e = Eccentricity of the tendon T = P = Prestressing force in the tendon moment equilibrium yields the relation, M = Ca = Ta = Pa, and, a = M/P - The shift of pressure line e/ measured from the centroidal axis is obtained as, e” = (a – e) = (M/P) – e -The resultant stresses at the top and bottom fibers of the section are expressed as, fsup = (P/A) + (Pe”/Zt) finf = (P/A) – (Pe”/Zb) where Zt and Zb are the section moduli of the top and bottom fibers, respectively.

## Slide 6: Example 6
A prestressed concrete beam with a rectangular section 120 mm wide by 300 mm deep supports a uniformly distributed load of 4 kN/m, which includes the self-weight of the beam. The effective span of the beam is 6 m. The beam is concentrically prestressed by a cable carrying a force of 180 kN. Locate the position of the pressure line in the beam.

## Slide 7: Example 6

## Slide 8: Example 7
A prestressed concrete beam of section 120 mm wide by 300 mm deep is used over an effective span of 6 m to support a uniformly distributed load of 4 kN/m, which includes the self-weight of the beam. The beam is prestressed by a straight cable carrying a force of 180 kN and located at an eccentricity of 50 mm. Determine the location of the thrust line in the beam and plot its position at quarter and central span sections.

## Slide 9: Example 7

## Slide 10: Example 8
A rectangular concrete beam 250 mm wide and 300 mm deep is prestressed by a force of 540 kN at a constant eccentricity of 60 mm. The beam supports a concentrated load of 68 kN at the center of a span of 3 m. Determine the location of the pressure line at the center, quarter span and support sections of the beam. Neglect the self-weight of the beam.

## Slide 11: Example 8

## Slide 12: Example 8